## Slide 1: Robustness Analysis
3 AFS Controllers: HINF, MIDAAS, ILAF
Margins checked at direct I/O used for each controller (e.g., ILAF controller uses symmetric L1/R1, Hinf uses independent L1/R1)
Complete controller that includes the SAS and autopilots is used to check margins
Individual RFS calculated at all individual criteria: Classical loop-at-a-time for: Input GM, Input PM, Output GM, Output PM; Multi-loop Input Disk Gain Margin
  Threshold criteria: 6 dB GM, 45o PM
Absolute RFS is based on Classical loop-at-a-time criteria only
Code: RobustnessAnalysisAP.m (2/14/2019)
Geri model includes actuator dynamics with 25 sec. time delay (4th order Pade) and sensor dynamics (no engine dynamics currently)

## Slide 2: SAS and Autopilots - description
Roll Damper
  Gain
  p to aileron
Pitch Controller (pitch attitude command)
  PI
  Theta error to elevator
Roll Controller (roll attitude command)
  PI
  phi error to elevator
Auto throttle (speed command)
  PI
  u error to thrust
Altitude hold
  Gain
  h error to theta command (pitch controller input)

## Slide 3: HINF AFS - description
4 inputs
  L1
  R1
  L4
  R4
8 outputs
  qcg [rad/s ]
  pcg [rad/s ]
  nzCBfwd [ft/s^2]
  nzCBaft [ft/s^2]
  nzLwingfwd [ft/s^2]
  nzLwingaft [ft/s^2]
  nzRwingfwd [ft/s^2]
  nzRwingaft [ft/s^2]
Fixed controller for all airspeeds
15 states
Targets 2 flutter modes

## Slide 4: MIDAAS AFS - description
4 inputs
  L1
  R1
  L4
  R4
8 outputs
  qcg [rad/s ]
  pcg [rad/s ]
  nzCBfwd [ft/s^2]
  nzCBaft [ft/s^2]
  nzLwingfwd [ft/s^2]
  nzLwingaft [ft/s^2]
  nzRwingfwd [ft/s^2]
  nzRwingaft [ft/s^2]
Fixed controller for all airspeeds
2 states
Targets 2 flutter modes

## Slide 5: ILAF AFS - description
1 Input
  Symmetric Body flaps (L1+R1)
2 outputs
  nzCBfwd [ft/s^2]
  nzCBaft [ft/s^2]
Gain scheduled with airspeed – a net gain, no change in dynamics.
3 states
Controller designed SISO: output is difference between accelerometers
Targets a single flutter mode

## Slide 6: Robust Margin Summary
HINF
Robust Flutter Speed: 40.8 m/s
Absolute Flutter Speed: 42.0 m/s
Individual RFS:
RFS due to PM at Input: 40.8 m/s
RFS due to GM at Input: 42.0 m/s
RFS due to PM at Output: 41.1 m/s
RFS due to GM at Output: 42.0 m/s
RFS due to GM at Multi-Input: 20.0 m/s
MIDAAS
Robust Flutter Speed: 36.3 m/s
Absolute Flutter Speed: 40.5 m/s
Individual RFS:
RFS due to PM at Input: 37.1 m/s
RFS due to GM at Input: 36.7 m/s
RFS due to PM at Output: 36.3 m/s
RFS due to GM at Output: 37.5 m/s
RFS due to GM at Multi-Input: 34.5 m/s
ILAF
Robust Flutter Speed: 31.2 m/s
Absolute Flutter Speed: 37.0 m/s
Individual RFS:
RFS due to PM at Input: 33.8 m/s
RFS due to GM at Input: 34.8 m/s
RFS due to PM at Output: 33.3 m/s
RFS due to GM at Output: 31.2 m/s
RFS due to GM at Multi-Input: 32.5 m/s

## Slide 7: HINF – Robustness Margins Results

## Slide 8: HINF – Robustness Margins Results

## Slide 9: HINF – Robustness Margins Results

## Slide 10: MIDAAS – Robustness Margins Results

## Slide 11: MIDAAS – Robustness Margins Results

## Slide 12: MIDAAS – Robustness Margins Results

## Slide 13: ILAF – Robustness Margins Results

## Slide 14: ILAF – Robustness Margins Results

## Slide 15: ILAF – Robustness Margins Results